# MATERIAL SAFETY DATA SHEET

# Compiled in accordance with Directives 2001/58EEC, 91/155 EEC, 1999/45/EEC, and 67/548/EEC

Date: 10/16/02

1. IDENTIFICATION OF PRODUCT AND COMPANY

## PRODUCT NAME:  SWEEPING LOG

# USE:  Treatment and removal of creosote in residential wood-burning appliance chimneys

COMPANY AND EMERGENCY PHONE NUMBER :

EUREXIM SECURIFLAME

18, rue de la Grosse Pierre

78540 VERNOUILLET-France

Tel.: 33 1 39 28 18 00 / Fax: 33 1 39 65 81 65

2.COMPOSITION INFORMATION ON INGREDIENTS

| Component | CAS # | EINEC/ELINCS | Danger Symbol Letter | R Phrase* | Percent Composition |
| --- | --- | --- | --- | --- | --- |
| Slack wax | 64742-61-6 | 265-165-5 | none | none | 51% |
| Wood sawdust | 9004-34-6 (cellulose) | 232-674-9 (cellulose) | none | none | 34% |
| Ammonium sulphate | 7783-20-2 | 231-984-1 | Xi | 36,37, 38 | 14% |
| Diphosphorous pentoxide (phosphorous pentoxide) | 1314-56-3 | 215-236-1 | C | 35 | 0.99% |
| Copper sulphate pentahydrate | 7758-99-8 | Unlisted | Xn, N | 22, 36/38, 50/53 | 0.12% |
| Amorphous silica | 112926-00-8 | Unlisted | Xn | 20 | 0.077% |

*R phrases provided under heading 16

3.HAZARDS IDENTIFICATION

Classification of preparation is not dangerous as per Annex II of 1999/45/EC.

4.FIRST AID PROCEDURES

INHALATION:  Inhalation of the preparation is not a concern but in the case of inhalation of combustion fumes remove person to fresh air.

Inhalation may produce nausea and irritation of the upper respiratory tract.  If symptoms persist, seek medical attention.

If breathing has stopped, administer artificial respiration/oxygen.

SKIN: Cool solid material is not expected to cause skin irritation.

Thermal burns may result from contact with hot material.  If hot melted material gets on the skin, quickly cool in water see a doctor for extensive burns. Do not try to peel the solidified material from the skin or use solvents or thinners to dissolve it.

EYES: On exposure to combustion fumes move person away from exposure and into fresh air.  Flush eyes with clean water.  If irritation or redness persists, seek medical attention.

For contact with molten material, gently open eyelids and flush affected eye(s) with cold water.  Seek immediate medical attention.

INGESTION: DO NOT INDUCE VOMIT; give large amounts of water. Call a physician.

# Anti-poison center (PARIS): 01 40 05 48 48

5.FIRE FIGHTING MEASURES

# FLAMMABLE PROPERTIES:

Flash point: 230° C

EXTINGUISHING METHODS:

Recommended: CO2, DRY CHEMICAL OR FOAM

Not recommended: DON'T USE WATER EXCEPT AS A FOG

HAZARDOUS COMBUSTION PRODUCTS:

Irritating and toxic gases or fumes may be released during a fire.

# PROTECTION EQUIPMENT: Respiratory and eye protection required for fire fighting personnel.  A self-contained breathing apparatus (SCBA) should be used for all indoor fires and for significant outdoor fires.

6.ACCIDENTAL RELEASE MESURES

Personal Precautions:  Remove all sources of ignition and any strong oxidizers.  Avoid inhalation of dust; wear safety glasses with side shields, long sleeves, and chemical resistant gloves.

Environmental Precautions:  Keep away from drains, surface and ground water, and soil.

7. HANDLING AND STORAGE

# HANDLING: Where prolonged and/or repeated skin and eye contact is likely to occur wear safety glasses with side shields, long sleeves, and chemical resistant gloves.

STORAGE: Store at ambient temperature in a dry place, general ventilation, and away from combustible materials/strong oxidizers.

SPECIFIC USE:  Burn in residential wood burning appliance only.  See manufactures instructions for details.

8. EXPOSURES CONTROLS PERSONAL PROTECTION

#### 8.1  Exposure Limit Values

## No exposure or biological limit values set for preparation.

Exposure and Biological Limit Values for Constituent Substances

## Slack Wax		OSHA  PEL: 2 mg/m3 (8 hr TWA, paraffin wax fume)

## ACGIH  TLV: 2 mg/m3  (8 hr TWA, paraffin wax fume)

UK HSE:  2 mg/m3 (8 hr TWA, paraffin wax fume)

UK HSE 6 mg/m3 (15 min, TWA STEL paraffin wax fume)

oral-rat: >5000 mg/kg

dermal-rat: > 2000 mg/kg

Wood Sawdust	OSHA PEL: 10 mg/m3 (8 hr TWA, nuisance dust)

Ammonium Sulphate	OSHA PEL:  not established

ACGIH TLV:  not established

orl-man TDLo:1500 mg/kg:GIT

orl-rat LD50: 3000mg/kg

ipr-mus LD50: 610 mg/kg

orl-dom LDLo: 3500 mg/kg

Diphosphorous	OSHA PEL: not established

## Pentoxide		ACGIH TLV:  not established

ihl-rat LC50: 1217 mg/m3/1H

ihl-mus LC50: 271 mg/m3/1H

ihl-rbt LC50: 1689 mg/m3/1H

ihl-gpg LC50: 61 mg/m3/1H

Copper			OSHA PEL:  1 mg/m3 dust, 0.1mg/m3 fume

Sulphate		ACGIH TLV: 1 mg/m3 dust, 0.2 mg/m3 fume

Pentahydrate		dni-hmn:lym: 76 micromole/l

cyt-rat/ast: 300 mg/kg

orl-hmn TDLo: 272mg/kg: LIV,KID,BLD

orl-hmn LDLo: 1088mg/kg

unk-man LDLo: 221 mg/kg

orl-rat LD50: 300 mg/kg

ipr-rat LD50: 18.7 mg/kg

ipr-mus LD50: 33 mg/kg

orl-dog LDLo: 60 mg/kg

scu-gpg LDLo: 62 mg/kg

orl-pgn LDLo: 1000 mg/kg

orl-dom LD50: 5 mg/kg

orl-mam LD50: 470 mg/kg

ipr-mam LD50: 7.5 mg/kg

orl-bwd LDLo: 300 mg/kg

Amorphous		OSHA TWA 6 mg/m3

silica

8.2 Exposure Control: Where prolonged and/or repeated skin and eye contact is likely to occur wear safety glasses with side shields, long sleeves, and chemical resistant gloves.  Use general ventilation.

9. PHYSICAL and CHEMICAL PROPERTIES

APPEARANCE: Brown wax/sawdust firelog

ODOR: Mild, none in its packaging.

PHYSICAL STATE: Solid  (28-cm long / 8 cm diameter.)

pH: 6

Boiling point:  350-650º C

Flash point:  230º C

Flammability:  Not Flammable

Explosive properties:  Not Explosive

Oxidising properties:  Not Oxidising

Vapour Pressure:  3 mm Hg

Vapour Density:  1.4

Density:  1 g/cc

Solubility:  Insoluble

Partition coefficient:  Large n-octanol/water partition coefficient

Viscosity:  3-30 mm2/s

Evaporation Rate:  <0.01

10. STABILITY/REACTIVITY

CHEMICAL STABILITY: Stable

INCOMPATIBILITY: Strong oxidizers

CONDITIONS TO AVOID:  Wet and/or high temperatures

HAZARDOUS DECOMPOSITION PRODUCTS:  Acidic gases produced on combustion

11. TOXICOLOGICAL INFORMATION

The product is contained in sealed waxed paper wrapper throughout its use and the diphosphorous pentoxide is contained in a wax matrix within the preparation.  Both minimize the potential of the diphoshorous pentoxide component into coming in contact with eyes, respiratory system or skin, therefore, irritation to skin, eyes or respiratory system will not occur through normal use. Due to the physical nature of the product ingestion is unlikely.

Human health effects may occur through ingestion of combustion residue due to the concentration of copper salts in the residue and through the inhalation of gases produced by combustion due to the decomposition/oxidation of ammonium sulphate and diphosphorous pentoxide ingredients producing acid gases. Human systemic effects due to the ingestion of combustion residue would include jaundice, unspecified urinary system effects and hemolysis. No significant adverse health effects form inhalation are expected to occur under normal conditions of use. However, exposure to the smoke at high levels while burning may be irritating to the nose, throat and lungs.  The irritating nature of the smoke precludes excessive unknowing exposure.

12. ECOLOGICAL INFORMATION

Most likely environmental effects are through the contact of the preparation or of its combustion residue with surface or ground waters allowing for the leaching of copper salts.  Soluble copper salts are used as biocides, are toxic to aquatic organism and are persistent in the environment.  The U.S.EPA’s aquatic criteria for copper are:

Freshwater, CMC (criteria maximum concentration) 13 micrograms/liter

Freshwater, CCC  (criteria continuous concentration) 9.0 micrograms/liter

Saltwater,  CMC 4.8 micrograms/liter

Saltwater, CCC 3.1 micrograms/liter

13. DISPOSAL CONSIDERATIONS

Disposal should be accomplished through an authorized person/licensed waste disposal contractor in accordance with local regulations.  Incineration of product may be carried out under controlled conditions, provided that local regulations for emissions are met.

14. INFORMATION RELATIVE TO TRANSPORT

## During transportation, keep dry and at ambient temperature.  Avoid sources of ignition and strong oxidizers.

15. REGULATORY INFORMATION

Prop. 65 California: Combustion of this manufactured sweeping log results in the emission of carbon monoxide, soot, and other combustion by-products which are known by the state of California to cause cancer, birth defects, or reproductive harm.

16. OTHER INFORMATION

This firelog has been tested and approved by Underwriters Laboratories, Inc. for consumer safety.

This firelog has been tested by OMNI-Test Laboratories, Inc. for its chimney cleaning capabilities, flue emissions, and chimney damage potential.

RELEVANT R PHRASES (see section 2):

R20		Harmful by inhalation

R22		Harmful if swallowed

R35		Causes sever burns

R36		Irritating to eyes

R37		Irritating to respiratory system

R38		Irritating to skin

R36/38		Irritating to eyes and skin

R50/53	Very toxic to aquatic organisms, may cause long-term advise effects in the aquatic environment

DISCLAIMER OF LIABILITY

The information in this MSDS was obtained from sources which we believe are reliable. HOWEVER, THE INFORMATION IS PROVIDED WITHOUT ANY WARRANTY, EXPRESSED OR IMPLIED, REGARDING ITS CORRECTNESS.

The conditions or methods of handling, storage, use and disposal of the product are beyond our control and may be beyond our knowledge. FOR THIS AND OTHER REASONS, WE DO NOT ASSUME RESPONSIBILITY AND EXPRESSLY DISCLAIM LIABILITY FOR LOSS, DAMAGE OR EXPENSE ARISING OUT OF OR IN ANY WAY CONNECTED WITH THE HANDLING, STORAGE, USE OR DISPOSAL OF THE PRODUCT.

This MSDS was prepared and is to be used only for this product. If the product is used as a component in another product, this MSDS information may not be applicable.